## Slide 1: Introduction and analysis of an energy index to evaluate arm motion quality in neuromuscular patients
Presented by: Pouria Nozari Porshokouhi
Advisors: Saeed Behzadipour
Maryam Hoviattalab
September 2016

## Slide 2: Outline
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works
Outline
Background
Future Works
Method
Proposed research
Objective
Literature review
Conclusion
Results

## Slide 3
CVA or Cerebro-Vascular accident
  Also referred to as a stroke
  The sudden death of some brain cells
  Caused by lack of oxygen amount carried to the brain by blood flow
    Due to blockage of an artery
    Due to Rupture of an artery
Background
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 4: Background
Gross Motion Rehabilitation
  The very first and early motion by which any improvement can be observed
  Efficient only when the exercises suit the patient’s level of capability, otherwise:
    Not helping out the patient any more
    The patient might droop and feel feeble
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 5: Background
Motion quality diagnosis in neuromuscular patients
  Diagnosis process
    Patients’ current level
    Patients’ improvement
  Subjective motion quality rating
    Individual errors might be involved
    Overlap among the levels in such tests
    Small amount of improvement might be neglected
  Brunnstrom test
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 6: Background
A suitable index needed to be proposed
  Defining a more precise measure on motion quality
  Strongly correlating with the qualitative indices
  Defining the nature of the body motion
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 7: Literature Review
Quantitative motion quality evaluation
Fitts’ Law
General Systems Performance Theory
Signal Processing
Kinematic Indices
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works
Fitts’ Law
  A mathematical relation between velocity, upper limb range of motion and target’s size
  (Kondarske, 1994)

## Slide 8: Literature Review
Fitts’ Law
  Yang et al., 2002
    5 young healthy males
    4 Vicon cameras with some markers
    2D polar Fitts’ law
    Indices of difficulty and performance
    Smoothness index
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 9: Literature Review
GSPT (General Systems Performance Theory)
  Evaluating the performance of a system
  Making up a relation among structure, function and performance
  Fischer et al., 1997
Structure
Function
Performance
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 10
Signal Processing
  Mostly applied when Inertial sensors utilized
  The output signal applied to create a pattern
  Zhang et al., 2011
    Motions advised by therapists performed by them
    Motions captured by IMU sensors
    Each motion segment signal obtained
    A system trained by these patterns
    Then the patients perform the motions
    Their motion deviation from the trained patterns obtained
Literature Review
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 11: Literature Review
Kinematic Indices
  Butler et al., 2012
    30 TD and 25 CP children
    Reach & grasp cycles done
    Based on 3D kinematics
    A pediatric upper limb motion index (PULMI)
    A proper negative correlation between the PULMI and MACS among CP (ρ=-0.78, p<0.0001)
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 12: Literature Review
Kinematic Indices
  Celik, 2010
    Trajectory Error
      Normal deviation from the desired path (a straight line)
    Smoothness of Movement
      Normal deviation from the velocity profile which generates the minimum jerk
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 13: Literature Review
Kinematic Indices
  Fakhar, 2013
    49 HP CVA+ 6 normal subjects
    Indices
      Number of fluctuations of Jerk
      Mean Jerk
      Angle of clavicle made with the transverse plane
      Elbow flexion
      Mean velocity
    Good correlation observed for
      Mean velocity
      Elbow flexion
      No. of fluctuations of jerk
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 14: Literature Review
Conclusion
  Some of the indices are too much complicated and yield no physical or tangible concept
  Desired level of reliability not achieved yet
  Most of the motion analysis systems utilized costly systems, such as Vicon 3D system
  Motion analysis systems needed markers
  Kinetic nature of the arm motion ignored
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 15: Objective
Introduction of an energy index
  Both kinematics and dynamics involved
  Seems to model the nature of the arm well
Classifying the motion quality of upper extremity
  Validation of the energy index with the Brunnstrom grades
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 16: Proposed Research
Milestones of the research
1
A musculo-skeletal model of arm developed
Compare the index values to Brunnstrom levels
4
Energy values normalized and the normal index obtained
3
The model simulated for actual motion data and the raw energy values obtained for subjects
2
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 17: Proposed Research
Method overview
Motion Database
Arm Kinematics
(Solved analytically via Matlab)
Elbow & Wrist Position
Muscle Energy Estimator
Metabolic Energy Normalizer
Normalized Energy Index Values
Check if the Energy index correlates with the Brunnstrom grades
Arm Dynamics
(Solved via OpenSim)
Metabolic Energy Raw Values
Joints’ Torque Trajectories
Joints’ Kinematics
Filtration
Filtered Elbow & Wrist Position
Brunnstrom Levels
Skeletal model
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 18
Conventional model of 4-DoF arm (redundant)
4-DoF arm model in OpenSim
  Delp S.L. et al -> Lower-limb
  Holzbaur K.R. et al. -> Upper-limb
Method
Full Body Model
Frame 3
Internal/External Rotation
Frame 1
Flexion/Extension
Frame 2
Abduction/Adduction
Frame 5
Pronation/Supination
Frame 4 Flexion/Extension
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works
Inactive in case the wrist is the end-effector

## Slide 19
4 DoFs of upper limb model in present study
Method
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 20
Anthropometric consideration (Winters, 2011)
Method
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 21
Kinematic Reliability
  The forward kinematics of the model solved for joints’ motion compared with the initial Cartesian motion data
  The motion generated for the arm in OpenSim compared to that of the Matlab
Both cases checked  Inverse Kinematics reliable 
Method
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 22
Dynamic verification
  Some simulations conducted on SimMechanics
  e.g. A trajectory for Shoulder Flexion (0-100 deg)
  Forearm considered massless
Method
SimMechanics
OpenSim
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 23
Dynamic verification
  Result: Torque Trajectories
Method
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 24
Muscle Energy Estimator (Zhu et al., 2011)
  2 muscles in pair at each DoF
  Only 1 muscle in a pair activated at each instant
  2 types of contraction considered for each muscle:
    Eccentric contraction
    Concentric contraction
Method
Biceps activated
Biceps activated
Triceps activated
Triceps activated
Triceps activated
Biceps activated
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 25
Muscle Energy Estimator (Zhu et al., 2011)
  Can replace AnyBody wherever the overall behavior is of interest
  2 muscles in pair at each DoF (Hill type muscles)
  Metabolic power formulation
Method
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 26
Normalization
  Why Normalization?!!!
    The index expected to evaluate the motion quality
    The metabolic energy depend on some other parameters
    Some important factors which come to mind at first look
      Individual movement habits
      Distance travelled by the hand
      Movement velocity
Method
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 27
Normalization
  Distance travelled by the hands
     Energy consumed per meter
     somehow normalized
Method
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 28
Normalization
  Individual movement habits and patterns
    Different amounts of energy obtained for two subjects
      Does it represent difference in their motion quality?!!!
    It might be due to different individual patterns
       Normalized value of the paralyzed/not dominant side divided by that of the healthy/dominant side
Method
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 29
Normalization
  Velocity
      Model: a simple pendulum in SimMechanics
      Input: a trapezoidal trajectory for velocity
      Output: Metabolic Energy vs. Max Velocity
        Motion: 0-110 deg
        100 different values
        for joint’s maximum
        angular velocity:
        (1-100 deg/s)
Method
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 30
Initial evaluation of the index
  Normal hand motion
  Simulated-disabled hand motion
  Consumed energy normalized by distance and velocity
Method
Motion type | Normal Energy | Distance travelled(m) | Time (s)
Horizontal, right, normal | 5200 | 9.13 | 15.53
Horizontal, left, normal | 5047 | 14.38 | 21.55
Horizontal, Left, disabled | 6229 | 14.13 | 26.70
Vertical, right, normal | 4685 | 17.07 | 18.35
Vertical, left, disabled | 6123 | 26.90 | 23.36
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 31
Clinical Data
  34 HP CVA patients + 6 normal subjects
  4 various types of motion for each subject
    Horizontal motion
    Vertical motion
    Diagonal motion
    Repetitive motion
  Motions captured by Kinect at 30 Hz
  Some outlier motion data observed and disregarded
Method
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 32
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works
Method
Filtration
  Apply the motion to the arm model
    1st and 2nd derivatives needed
    The motion data contains a noisy part
      Derivation might lead to really massive jumps in velocity, …
      Filtration required
  B-Spline method
    Cubic B-Spline (of 4th order) \(Mobini, 2015)

## Slide 33
A shortcoming lies within the model
  An inherent singular configuration involved
  Whenever the elbow flexion relatively infinitesimal
   Problem with solving the shoulder rotation DoF
   Shoulder rotation torque changes erratically
   The shoulder rotation torque neglected in energy summation
Results
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 34
Results
 | Normalized by: Distance travelled Individual patterns | Normalized by: Distance travelled Velocity of motion Individual patterns
Horizontal |  | 
Vertical |  | 
Diagonal |  | 
Repetitive |  | 
Motion Type
Normalization
Type
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 35
Results (Horizontal Motion)
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 36
Results (Vertical Motion)
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 37
Results (Diagonal Motion)
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 38
Results (Repetitive Motion)
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 39
 | Normalized by: Distance travelled Individual patterns |  |  | Normalized by: Distance travelled Velocity of motion Individual patterns |  | 
 | PT | OT | Mean | PT | OT | Mean
Horizontal | -0.32 | -0.38 | -0.36 | -0.37 | -0.40 | -0.40
Vertical | -0.21 | -0.31 | -0.27 | -0.43 | -0.52 | -0.48
Diagonal | -0.73 | -0.63 | -0.68 | -0.84 | -0.81 | -0.84
Repetitive | -0.32 | -0.37 | -0.35 | -0.50 | -0.60 | -0.56
Mean | -0.59 | -0.64 | -0.63 | -0.67 | -0.73 | -0.72
Normalization
Type
Motion
Type
Results (Cross Correlation Values)
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 40
Qualitative indices may confuse the therapists
  Individual disagreements
  Due to the overlaps
  Lower levels of improvements may be neglected
No good reliability in kinematic indices
  Not modeling the kinetic nature of the limb motion
  Some indices too complicated
An energy index proposed
  Both Kinematics & Dynamics taken into account
  Normalized to get to energy index
  Correlation analysis carried out
Conclusion
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works

## Slide 41
To be compared to other kinematic indices
Energy index might be unable to classify on its own
  Maybe better to exploit some other indices in company with the energy index
More controlled experiments to be conducted
Future Works
Outline
Background
Literature Review
Objective
Proposed Research
Method
Results
Conclusion
Future Works